## Slide 1: UR 2 Robotic Arm Project Daniel Oliver

## Slide 2: Project objective description
Identify 2-inch triangular or square steel plate parts placed on white surface 12” away.
Move plates to two different stacks at a 90° angle from the original location.

## Slide 3: Literature Review and Market Research
For pick and place applications robotic arms often utilize a computer vision system.
The vision system allows the arm to effectively get to the desired object and then move it to the proper location.
Common applications of vision guided robots are
  Loading/unloading parts from conveyors and feeding systems
  Loading/unloading nested parts from trays or boxes
  Part placement, assembly and packaging
  Racking and de-racking
  Palletizing and de-palletizing
  Bin picking of random parts
Notes: https://www.visiononline.org/blog-article.cfm/Vision-Guided-Robotics-for-Pick-and-Place-Applications/71

## Slide 4: Designs Considered
Initial designs

## Slide 5: Designs Considered
Initial CAD Model
Second CAD Model

## Slide 6: Proposed Design
Final design

## Slide 7: Budget
12 kg servo motor: $5.25
20 kg servo motor: $13.50
35 kg servo motor: $38.99
Electro magnet: $9.29
6” turn table: $6.49
Webcam: already had
Total: $91.51
Bearings: $0.60 (x3)
Metal servo horn: $1.40 (x3)
U-channel: $11.99
3D printed joints: $
Wood: already had
Erector set parts: already had

## Slide 8: Summary of Design
Wooden base with turn table.
3D printed joints
Aluminum U-channel arm linkages
Erector set used for lever arms

## Slide 9: Summary of Design
Motors
12kg/cm for the base rotation
20kg/cm for the second link
35kg/cm for the third link
Aluminum servo horns for attaching motors to the pivot arm.

## Slide 10: Summary of Design
Base
Wooden base
6” turn table

## Slide 11: Summary of Design
Arm linkages
U-channel used for arm linkages
3D printed joints
22 mm bearings
9/16” dowel

## Slide 12: Lessons Learned
EmguCV for shape detection
Arduino control for servos
Equations of motion of a two link robot arm

## Slide 13: Recommendations for future development and conclusions
Try to minimize the complexity of your kinematics
Try to reduce weight of robot arms
Add counterweight to reduce base movement.